## Slide 1: Safe Systems and Urban Development
Eric Dumbaugh: A Model for Safe Systems in Urban Environments
Louis Merlin: The Built Environment and Traffic Safety
FAU Double Header!

## Slide 2: Towards Safe Systems in the United States Industrial Systems, Behavioral Economics, and Social Psychology

## Slide 3: Outline
Counterfactual Reasoning Contemporary Approach to Crash Analysis
The Limits of Counterfactual Reasoning The Case of Raquel and A.J. Nelson
A Broader Perspective Lessons from Urban Roadside Safety
Conclusion: A Model for Safe Systems

## Slide 4: Counterfactual Reasoning
Part 1:

## Slide 5: Psychological Processes:
Antecedent → Consequence
Counterfactual Reasoning: A form of logic that falsifies antecedents to determine whether they negate consequences.
Form:

## Slide 6: Constructing Counterfactual Content
Outcome Closeness: We focus on antecedents that are immediately proximate to consequences.
Outcome Normality: Exceptional outcomes are presumed to follow from exceptional antecedents. We construct counterfactuals that shift the exceptional antecedent to its “normal” value.
Extant Norms: Counterfactual content is based on social norms of expected behavior (which are modifiable and socially constructed).
Source: Roese, 1997
Notes: Individuals construct counterfactuals based on whichever antecedent was exceptional
- example: Kahneman

## Slide 7: Current Safety Approach
Errors and Violations
Crashes
Engineering Defenses
Individual

## Slide 8: Counterfactual Reasoning: Critical Factors
Source: NHTSA, 2015

## Slide 9: Counterfactual Reasoning: Driver Error
Source: NHTSA, 2015
Notes: Recognition error, which included driver’s inattention, internal and external distractions, and inadequate surveillance, was the most (41% ±2.2%) frequently
assigned critical reason.
Decision error such as driving too fast for conditions, too fast for the curve, false assumption of others’ actions, illegal maneuver and misjudgment of gap or others’ speed accounted for about 33 percent (±3.7%) of the crashes.
performance error such as overcompensation, poor directional control, etc. Sleep was the most common critical reason among non-performance errors that accounted for 7 percent (±1.0%) of the crashes.
Other driver errors were recorded as critical reasons for about 8 percent (±1.9%) of the drivers.

## Slide 12: Traffic Fatalities in the US
Source: NHTSA, 2017
Notes: 6% increase

## Slide 13: Blame the Victim
“It’s still the same things that are killing drivers — belts, booze, and speed.”
  Jonathan Adkins, Executive Director of the Governors Highway Safety Association
Source: New York Times, 2/15/2017

## Slide 14: The Case of Raquel and A.J Nelson
Part 2:
“Blaming individuals is more emotionally satisfying than targeting institutions.”
- James Reason

## Slide 15: The Limits of Counterfactual Reasoning: The Case of Raquel and A.J. Nelson

## Slide 16
Errors and Violations
Crashes
Engineering Defenses
Individual
Error-Producing Conditions
Environmental
Management Decisions and Organizational Processes
Organizational
Notes: Environmental – the location of a bus stop adjacent to a housing complex, in the absence of a crosswalk, creates conditions that encourage errors and violations.
Organizational – Policies on bus stop placement and the location of protected crosswalks lead to the creation of environments that encourage erros and violations

## Slide 17
Active Failure: Actions taken by people with direct responsibility for the system, who may make slips, lapses, or mistakes.
Latent Failure: Policy decisions that result in dormant conditions that, when combined with active triggers, lead to crashes.
Notes: The bus stop policy was not adopted to kill people, but to make transit more accessible. But it created a latent condition that, when activated by Raquel Nelson’s decision, resulted in the death of A.J Nelson.
Slips: Actions not carrier out as intended or planned, e.g., misreading road signs and exiting a roundabout on the wrong road
Lapses: missed actions or omissions, e.g., failing to do something due to lapses of memory or attention (not treating a powerless light as a four-way stop).
Mistakes: Wrong actions carrier out due to a faulty plan or action, e.g., someone believing something to be correct when it was, in fact, wrong.
Violations: Deliberate illegal actions, i.e., somebody doing something knowing it to be against the rules.

## Slide 18
Error-Producing Conditions
Management Decisions and Organizational Processes
Errors and Violations
Crashes
Engineering Defenses
Individual
Environmental
Organizational
Latent Error Pathway
Active Failure Pathway
Notes: Latent error pathway: policies applies without knowledge of later consequences.

## Slide 19: Urban Roadside Safety
Part 3: Illustration

## Slide 20: Illustration: Urban Roadside Safety
Presumed Roadside Encroachment Pattern
Presumption is that run-off-roadway events are random and unpreventable.
If so, then rates of run-off-roadway events should be relatively constant.
Studies of two-lane, rural roads support this conclusion…

## Slide 21
Drivers will err, make mistakes, and engage in behaviors that result in crashes and injuries.
Driver errors are random and unpreventable.
The best strategy for addressing driver errors is to ensure that all roadways are “forgiving” to such errors when they occur.
Theoretical Precepts:
Errors and Violations
Crashes
Engineering Defenses
Individual

## Slide 22: Research Question: Is This Unsafe?

## Slide 23: Basis for Urban Clear Zone Policy
Source: Turner and Mansfield, 1990
The Evidence:
The majority of urban tree-related crashes occur less than 30 ft from the travel-lane
Study Conclusion: 30 ft clear zones in urban areas are desirable for safety.

## Slide 24: Crash Site Investigation: 27 Miles of Urban Arterials in Central Florida
SR 15, DeLand (Woodland Blvd)
SR 44, DeLand (New York Ave)
SR 40, Ocala (Silver Springs Blvd)
Notes: Total – 27.25 Miles of roadway

## Slide 25: Revisiting Turner and Mansfield Findings

## Slide 26: Crash Probability Mirrors Setback Distribution
Notes: Lateral offset doesn’t matter. Regardless of fixed-object setback, the probability of crash is the same.

## Slide 27: Conventional (Correlational) Analysis: Negative Binomial Regression
Independent Variables
  Shoulder Width
  Fixed Object Offset
  Livable Street Dummy Variable
Control Variables
  ADT
  Number of Lanes (2 or 4)
  Lane Width
  Median Width

## Slide 28: Conventional Theory: Correlational Analysis of Engineering Countermeasures
“The wider the clear zone, the safer it will be” (TRB, 2004).
Expected Results

## Slide 29: Correlation: Paved Shoulders
Wider shoulders are consistently associated with increases in roadside and midblock crashes

## Slide 30: Correlational: Fixed Object Offsets
Wider fixed object offsets are associated with decreases in fixed-object crashes, but have no effect on (and may even slightly increase) midblock crashes

## Slide 31: Test Results: Livable Streets
Livable street treatments are consistently associated with decreases in fixed-object and midblock crashes

## Slide 32: Livable Streets
None of the livable streets had offsets greater than 4 feet
Not a single injurious roadside crash on any of the livable street treatments
Not a single fatality occurred on any of these roadways

## Slide 33: A Systems Approach: Systematic Crash Reconstruction
Illustrative Urban Fixed-Object Crash
83% of tree and pole crashes occurred behind an intersection or driveway on higher-speed roadway sections.
Field examination (Florida) of roadside crash locations:

## Slide 34: Urban Roadside Crashes
Representative Urban Fixed-Object Crash
Systematic Pattern:
Higher operating speeds along primary arterial
Driver attempt to turn onto a driveway or side street at higher speeds
Approach speed results in a roadside encroachments across the adjacent driveway or side street

## Slide 35: Latent Error
Organizational Factors
Functional Classification
Design Speed
Driveway and Development Policy
Clear Zone Policy

## Slide 36: a Model For Safe Systems
Part 4: Conclusion

## Slide 37: A Model for Safe Systems
Error-Producing Conditions
Management Decisions and Organizational Processes
Errors and Violations
Crashes
Engineering Defenses
Individual
Environmental
Organizational
Zoning Ordinances
Subdivision Regs
Regional Dev. Plans
Functional Class
Performance Measures (LOS)
Geometric Design
  Design Speed
  Design Vehicle
Traffic Control
Driveway Policies
ROW Allocation
  Bike
  Ped
  Transit
Education
Licensure
Enforcement
Legal Sanctions
Passive safety
Intelligent vehicles
Traversable hardware

## Slide 38: FAU Activities: From Roadmap
Identifying the Safety Information Needs of Major Cities in the U.S.
  This study seeks to understand how cities in the U.S. address the issue of traffic safety, as well as to identify the research, information, and guidance they view as being most essential to advancing their safety needs.
Safe Systems Synthesis & Summit Phase 1
  This effort will entail a review of the literature on safe systems and a leadership summit to engage key stakeholders in the development of a single, working definition of the safe systems concept.
Completing the Picture of Traffic Injuries: Understanding Data Needs and Opportunities for Road Safety (Led by UT-K)
  To complete the picture of crashes and determine which elements of data that exist outside of conventional crash data can contribute to this picture, and to identify innovative statistical, probabilistic, and big data visualization tools to link crashes with other records.

## Slide 39: Identifying the Safety Information Needs of Major Cities in the U.S.
Area 1:

## Slide 40: R1: Status
Focus Group: 10/30/2017
    We are repeating the mistakes of the past…
Survey: Pending

## Slide 41: Safe Systems Summit and Literature Review
Area 2:

## Slide 42: Literature Review: Elements
  Open vs. Closed Systems
  Defining Errors/Risk
  Latent Factors (Systematic Error)
  Speed Management
  Self-Explaining Roads (Schema/Schemata)
  Safety Culture
  Models and Processes

## Slide 43: Safe Systems Summit
Part 1: Safe Systems Concepts
Part 2: Implementation

## Slide 44: SUMMIT PART 1: CONCEPTS
Systems Perspective
    KEYNOTE: Organizational/Systems Theory (James Reason)
    Safety-Conscious Planning (Michael Meyer/Susan Herbel)
Safe Speeds (Leah Shahum)
Safe Streets (Janette Sadik-Khan)
Safe Users
    Safety Culture (Nicholas Ward)
    Social Science/Traffic Psychology Perspective
Safe Vehicles
    Vehicle Manufacturers
    Connected/Automated Vehicles

## Slide 45: SUMMIT PART 2: IMPLEMENTATION
Industry Roundtable
  NACTO
  Vision Zero Network
  AASHTO
  ITE
City Roundtable
  NYC
  Chicago (?)
  Los Angeles (?)
  Fort Lauderdale (?)